## Slide 1
MEDS-S1 R-03: Instruction Cache, Data Cache, Zicbom, and meds_sram_wrapper
Presented by: Muhammad Usman
August 20th, 2026

## Slide 2
SCOPE & CONTEXT
Building the cache subsystem abstraction for MEDS-S1
12-week Priority P1 project
in MEDS-S1 WP7
Delivering a parameterized I$ and D$ with meds_sram_wrapper abstraction
Implements Zichom extension
CBO.CLEAN, CBO.INVAL, CBO.FLUISH
MEDS-S1 SoC
Instruction Cache (I$)
Parameterized
Data
Cache (D$)
Parameterized
meds_sram_wrapper
Abstraction Layer
Zichom Extension
CBO.CLEAN | CBO.INVAL | CBO.FLUSH
12-WEEK PROJECT TIMELINE
WEEKS 1–4
Design & Architecture
WEEKS 5–9
Implementation & Integration
WEEKS 10–12
Verification & Delivery
PROJECT

## Slide 3
ZICBOM — THE SOFTWARE COHERENCY CONTRACT
CPU / SOFTWARE
ZICBOM COMMANDS
CBO_CLEAN
CBO.INVAL
invalidate stale lines
CBO.FLUISH
clean + invalidate atomic
CACHE
data cache
STOREBUFFER
ordered interaction
Software contract today — hardware coherency arrives in v2
CBO.CLEAN
write back before DMA reads
CBO.INVAL
invalidate after DMA writes
CBO.FLUISH
atomic clean and invalidate
Correct interaction with Store Buffer
write back dirty lines
COHERENT
ACCESS
DMA
device
Issues zicbom command

## Slide 4
CPU CORE
CACHE CONTROLLER
2-WAY SET-ASSOCIATIVE CACHE
WAY 0
TAG ARRAY
DATA ARRAY
(64B LINE)
WAY 1
TAG ARRAY
DATA ARRAY
(64B LINE)
NON-CACHEABLE PMA REGIONS (MMIO)
WRITE BUFFER (WRITE-BACK)
MAIN MEMORY
2-way set-associative
64-byte (512-bit) cache lines
Write-back policy with dedicated write buffer
Blocking design
misses stall the pipeline
Configurable sizes
S1-Nano: 8KB
S1/Base/AI: 16KB
CACHE MICROARCHITECTURE (SPEC §15)
BYPASS PATH
=>"I$ is structurally identical but read-only (no write buffer, no CBO.CLEAN)"

## Slide 5
(SPEC $11)
CPU LOAD/STORE REQUEST
addr, type, priv
D$ TAG LOOKUP
address-to-tag match
PMA/PMP CHECKER
parallel attribute evaluation
CACHEABLE
IDEMPOTENT
DECISION LOGIC
combine results
ACCESS PROCEEDS? CACHE THIS ACCESS?
RESULT
ALLOW / DENY ACCESS
CACHE / BYPASS (NO CACHE POLLUTION)
Attributes checked
in parallel with tag lookup
Determines access and caching behavior
Prevents cache pollution from MMIO regions
PMA/PMP PARALLEL CHECKING
ATOMIC

## Slide 6
meds_sram_wrapper – The Abstraction Layer
meds_sram_wrapper
Abstraction Layer
Memory Array
(Tags / Data / Register File
/ TLB / FIFOs)
Output
Register
addr
rdata
Registered Read
(1 Cycle)
Register File
FIFOs
Mandatory wrapper for all memory arrays
No direct memory instantiations in core RTL
Strict 1-cycle registered read outputs for timing closure
PARAMETERS
DATA_WIDTH
ADDR_WIDTH
DEPTH
Tags
Data
TLB
clk
wen
wdata

## Slide 7
WRAPPER IMPLEMENTATION - THREE MODES
BEHAVIOURAL
SystemVerilog arrays for fast Verilator simulation
mem []
BRAM
Xilinx RAM36E1 primitive for KC705 FPGA
RAMB36E1
ADDR
EN
DOUT
DOA
ASIC
Macro stub for future tape-out ensuring architectural portability
SRAM_MACRO
ADDR
DOUT
DOA
DIN
DIN
EN

## Slide 8
KEY DESIGN DECISIONS
& RATIONALE
01
Blocking over non-blocking
02
Software coherency over hardware
03
Unified wrapper architecture
Chosen for v1 stability and predictable timing.
Non-blocking deferred to v2.
Zicbom software contract simplifies v1.
Hardware coherency deferred.
Ensures ASIC-clean RTL and portability.
Avoids FPGA-specific primitives in core logic.

## Slide 9
DELIVERABLES & ACCEPTANCE
(12 WEEKS)
RTL DELIVERABLES
I$ and D$ FSMs in rtl/cache/cache/ meds_sram_wrapper.sv inrtl/common/
VERIFICATION DELIVERABLES
Unit testbenches covering hit, miss, and eviction scenarios
DOCUMENTATION DELIVERABLES
Zicbom Software Contract note delivered to BSP team
METRICS DELIVERABLES
Baseline hit-rate measurements published for v1

## Slide 10
W1-2
Spec Review & Zicbom Note
W3-4
SRAMWrapper Implementation
W5-7
W8-10
Data Cache & Write Buffer
W11-12
Zicbom Logic & Testbenches
DEFINITION OF DONE
No inferred latches
CBO semantics verified against DMA testbench
Hit rates published
CI lint clean
MILESTONES & DEFINITION OF DONE
Instruction Cache